Forward Pass Project Results
Batch profiling results for basic forward convolution kernel:
Batch Size Op Time 1 Op Time 2 Total Execution Time Accuracy / 100 3.90226 ms 5.1347 ms 1.276 s .86 / 1000 11.0889 ms 48.1185 ms 11.516 s .886 / 10000 23.2205 ms 146.022 ms 1 min 40.687 s .8714
Weight matrix in constant memory
Which optimization did you choose to implement? Explain why did you choose that optimization technique. / I chose to implement a weight matrix in constant memory because I thought it would make the kernel more memory efficient since all of the operations can be stored and reused when needed from one single location.
How does the optimization work? Did you think the optimization would increase performance of the forward convolution? Why? Does the optimization synergize with any of your previous optimizations? / This optimization works by utilizing a matrix placed in constant memory to act as a filter over the various input images in the fashion data set. It is very memory efficient as constant memory is faster to access thus reducing the bandwidth requirements. I thought that this optimization would increase performance of the forward convolution since the data we would be dealing with would be anywhere from 100 to 10000 in terms of batch size, so the convolution would be expedited if there were less memory transactions required due to the matrix allowing better data accessibility. This optimization synergizes well with tiling and other shared memory techniques.
Batch profiling results:
Batch Size Op Time 1 Op Time 2 Total Execution Time Accuracy / 100 .226164 ms .839785 ms 0m 1.220s .86 / 1000 2.10433 ms 8.13764 ms 0m 10.177s .886 / 10000 20.6525 ms 81.62 ms 1m 40.276s .8714 / Was implementing this optimization successful in improving performance? Why or why not? / nsys Profile data: / The time (%) displayed by the CUDA Kernel Statistics show that 65.0% of time was taken by the cudaMemcpy. Compared to the figure of 71.6% of time needed for cudaMemcpy from the baseline code measured for Milestone 2, this means that there was a reduction of over 6% in time. This can be attributed to successfully implementing the weighted matrix in constant memory which is why cudaMalloc increases from 15.7% to 29.1%. We can conclude that this optimization was successful due to lowered OP times (~102ms) and the reduction in time taken by cudaMemcpy. / Nsight-Compute Profile data: / Based on the Nsight-Compute data, we can observe that there were high amounts of SM and Memory utilization at figures of approximately 85% and 70% respectively which are relatively high figures compared to 75% and 60% respectively from Milestone 2, but it is important to look at the memory workload analysis. Judging by how the L1 and L2 Cache have hit rates of approximately 95%, this means that the optimization of implementing a weighted matrix in constant memory is memory efficient and we were successful in increasing performance.
Modified code: / Code also modified in conv_forward_gpu_prolog.

Tiled shared memory convolution
Which optimization did you choose to implement? Explain why did you choose that optimization technique. / The next optimization I chose to implement was a tiled shared memory convolution because I thought it would allow for more hardware resources like memory to be used efficiently and enable parallelism across multiple threads at the same time.
How does the optimization work? Did you think the optimization would increase performance of the forward convolution? Why? Does the optimization synergize with any of your previous optimizations? / This optimization works by dividing data into rectangular tiles and storing them in shared memory where convolution is carried out on all tiles simultaneously. I thought this optimization would increase performance of the forward convolution since it would reduce the bottleneck of memory bandwidth requirements by improving cache utilization and take advantage of parallelism. This optimization can synergize well with the implementation of a weighted matrix in constant memory as both techniques have a common goal of increasing memory efficiency and reducing data fetching.
Batch profiling results:
Batch Size Op Time 1 Op Time 2 Total Execution Time Accuracy / 100 .312647 ms .675611 ms 0m 1.263s .86 / 1000 2.97889 ms 6.45686 ms 0m 9.802s .886 / 10000 29.624 ms 64.7542 ms 1m 36.691s .8714 / Was implementing this optimization successful in improving performance? Why or why not? / nsys Profile data: / Based on the data displayed for the CUDA API Statistics, cudaMemcpy takes 77.6% time which is approximately 5% more usage of that API call from Milestone 2 at 71.6% and additionally the cudaDeviceSynchronize went down from 11.2% to 7.0%. This data could be attbuted to utilizing more shared memory and the over 4% reduction in the cudaDeviceSynchronize could be interpreted as the code parallelizing more, thus the kernel having less of a need for that API call and the optimization being successful as also justified by the reduced OP time of approximately 95 ms. / Nsight-Compute Profile data: / This Nsight-Compute data shows that this optimization utilizes the same amount of SM as the weighted matrix in constant memory implementation (thus about approximately 7% more SM than Milestone 2) but actually uses less Memory at approximately 58% versus ~60% utilization for Milestone 2. This means that the tiled implementation in shared memory is a boost in performance as it makes better use of the memory bandwidth and requires less accesses.
Modified code:

Tuning with restrict and loop unrolling
Which optimization did you choose to implement? Explain why did you choose that optimization technique. / I chose this optimization technique because by restricting pointers and unrolling the main for loop in the kernel I thought that performance would be increased due to the reduction of memory access latency.
How does the optimization work? Did you think the optimization would increase performance of the forward convolution? Why? Does the optimization synergize with any of your previous optimizations? / The optimization works by allowing the compiler to optimize memory accesses by assuming that memory pointed to by a restricted pointer is not aliased by any other pointer. This means this optimization would increase the performance of forward convolution since the there would be improved cache utilization and reduced memory access latency. Loop unrolling would also boost performance as it would increase task parallelism. Another type of optimization that could go along with this technique is kernel fusion.
Batch profiling results:
Batch Size Op Time 1 Op Time 2 Total Execution Time Accuracy / 100 .231634 ms .83974 ms 0m 1.284s .86 / 1000 2.14323 ms 8.19904 ms 0m 10.354s .886 / 10000 21.4202 ms 81.7411 ms 1m 36.428s .8714 / Was implementing this optimization successful in improving performance? Why or why not? / nsys Profile data: / According to the data above for the CUDA API calls there is over a 5% increase in cudaMemcpy from 71.6% (Milestone 2) to 76.8% and a decrease in cudaDeviceSynchronize calls from 11.2% (also Milestone 2) to 7.5%, meaning the parallelism in the code increased as there was less need for cudaDeviceSynchronize and additionally due to the reduced memory access latency and utilization of the cache the cudaMemcpy calls went up. This optimization is thus a success in improving performance as the previously mentioned advantages helped to achieve an OP time of approximately 103 ms. / Nsight-Compute Profile data: / This optimization is an improvement over the baseline because we can see that uses approximately 57% of SM and 93% of memory compared to approximately 75% and 60% from Milestone 2. The L1 Cache and L2 Cache are also approximately 96% and 95% meaning that this optimization is a boost in performance as it reduces memory access latenc
Modified code:

Using Streams to overlap computation with data transfer
Which optimization did you choose to implement? Explain why did you choose that optimization technique. / I chose the optimization technique of implementing streams to overlap computation with data transfer because I thought it would make the code more seamless by reducing the bottleneck of time required for data transferred and that the streams would synergize with each other in order to further the performance.
How does the optimization work? Did you think the optimization would increase performance of the forward convolution? Why? Does the optimization synergize with any of your previous optimizations? / This optimization works by dividing the device resources into different streams which are all tasked with different operations such as data transfer or convolution. These streams can work hand in hand with one another to help one another complete their tasks and this significantly cuts down on the time needed for data transfer as it is done concurrently with the convolution. As a result of the multifaceted capabilities of streams, the performance is enhanced by cutting down on time and increasing parallelism. This optimization technique can synergize with techniques like memory pooling or batching to reuse device memory for operations.
Batch profiling results:
Batch Size Op Time 1 Op Time 2 Total Execution Time Accuracy / 100 .000685 ms .001195 ms 0m 1.231s .86 / 1000 .000758 ms .000903 ms 0m 11.159s .886 / 10000 .00071ms .001263 ms 1m 48.981s .8714 / Was implementing this optimization successful in improving performance? Why or why not? / Based on the CUDA API Statistics it seems that clearly cudaMemcpyAsync is called the most for 86.2% of the time compared to cudaMemcpy being called for 71.6% of the time in Milestone 2. This change can be attributed to the fact that we are utilizing streams to simultaneously transfer data and compute the convolution, vastly enhancing the performance time. The only potential cause for concern though is that the OP times are in the ~.001 ms for this optimization method meaning that although this was successful we are unsure as to what extent the performance was enhanced. / Nsight-Compute Profile data: / For this implementation of stream optimization, the SM and Memory usages are very high because the streams handle both the convolution and data transfer of the kernel, meaning that the code is an improvement due to it utilizing the hardware resources of the GPU to their fullest to achieve the kernel’s task. The only underlying issue is still the fact that the OP times are somewhat suspect meaning that there must be underlying data points that need to be measured that I have not found on Nsight_Compute.
Modified code: / In conv_forward_gpu_prolog: